## Slide 1
Oi
Dry
48 hours (min.), 65 °C
Weigh (record)
(soon after removal from oven)
Oe
Sieve
(if samples very wet, dry first, also kills ticks)
Dry (48 hours (min.), 65 °C)
(On sieve, organic material)
Weigh (record)
(soon after removal from oven)
Dry (48 hours (min.), 65 °C)
(Through sieve, mineral material)
Grind
Roller Mill (24 hours)
Weigh (record)
(soon after removal from oven)
Grind
Large mesh Mill Grinder
Then subsample (mix well, grind about 2 handfuls), use small mesh Wiley grinder (20 mesh)
Grind
Large mesh Mill Grinder
Then subsample (mix well, grind about 2 handfuls), grind through small mesh Wiley grinder (20 mesh)
Soil C and N analysis, and archive